## Slide 1: The Impact of Droughts on the Human Right to Water in California
Ben Rachunok, PhD
rachunok@stanford.edu

## Slide 2: Two ongoing crises in California
Water Affordability
  Water rates rising faster than inflation across the US
  In California, over 1,000,000 people lack access to clean, affordable, drinking water
California Drought Monitor
July 2021
Residential Water Rates, 2010-2015
Droughts
  California continuing to face severe drought conditions
Circle of Blue Water Rate Survey, 2019

## Slide 3: Human Right to Water (HR2W)

## Slide 4: Water Affordability & Accessibility
Over 1,000,000 people in California lack access to clean, affordable drinking water
Likely worsened by droughts
  Additional stress on water systems and utilities
Notionally
  Sourcing additional water is more expensive --> costs passed on to rate-payers
  Curtailing water use reduces utility revenue which gets re-couped through fees
  Mitigation actions (particularly demand-side) reduce water access below acceptable minimums

## Slide 5: Water Affordability & Accessibility
Over 1,000,000 people in California lack access to clean, affordable drinking water
Likely worsened by droughts
  Additional stress on water systems and utilities
Notionally
  Sourcing additional water is more expensive --> costs passed on to rate-payers
  Curtailing water use reduces utility revenue which gets re-couped through fees
  Mitigation actions (particularly demand-side) reduce water access below acceptable minimums

## Slide 6: Water Affordability & Accessibility
Over 1,000,000 people in California lack access to clean, affordable drinking water
Likely worsened by droughts
  Additional stress on water systems and utilities
Notionally
  Sourcing additional water is more expensive --> costs passed on to rate-payers
  Curtailing water use reduces utility revenue which gets re-couped through fees
  Mitigation actions (particularly demand-side) reduce water access below acceptable minimums

## Slide 7: Water Affordability & Accessibility
Over 1,000,000 people in California lack access to clean, affordable drinking water
Likely worsened by droughts
  Additional stress on water systems and utilities
Notionally
  Sourcing additional water is more expensive --> costs passed on to rate-payers
  Curtailing water use reduces utility revenue which gets re-couped through fees
  Mitigation actions (particularly demand-side) reduce water access below acceptable minimums

## Slide 8: Water Affordability & Accessibility
Over 1,000,000 people in California lack access to clean, affordable drinking water
Likely worsened by droughts
  Additional stress on water systems and utilities
Notionally
  Sourcing additional water is more expensive --> costs passed on to rate-payers
  Curtailing water use reduces utility revenue which gets re-couped through fees
  Mitigation actions (particularly demand-side) reduce water access below acceptable minimums

## Slide 9: Drought Mitigation Actions
Presently focusing on drought mitigation
E.g. Available water supply <= water demand

## Slide 10: Drought Mitigation Actions
Presently focusing on drought mitigation
E.g. Available water supply <= water demand
Building new infrastructure
Buying water on the spot-market
Transfer water from other utilities/wholesalers
Supply Side Examples

## Slide 11: Drought Mitigation Actions
Presently focusing on drought mitigation
E.g. Available water supply <= water demand
Building new infrastructure
Buying water on the spot-market
Transfer water from other utilities/wholesalers
Residential water conservation
Turf replacement
Progressive rate structures
Supply Side Examples
Demand Side Examples

## Slide 12: Our Model
Developing metrics that reflect community needs:
Affordability:
Access:

## Slide 13: Water Rates
6 CCF (considered bare minimum for a family of 3) $78.54
10 CCF (Normal by some sources for a median family) $134.70
Residential Bill = 13.55 + 1(CCF) + 9.03(0-5CCF) + 10.86(6-7CCF) + 12.78(8-9CCF) + 15.74(CCF 10+ )
Yellow: Fixed Charge or Ready to Serve Charge
Red: Volumetric Charge

## Slide 14: How do water rates change when conservation is enacted?
Conservation requirements mean less water used, less revenue for utilities
Revenue recovery accomplished through drought surcharges (right)
Flat rate increase to fixed charge
Over half of drought surcharges work this way (Feinstein 2018)
Surcharges for example utility in California

## Slide 15: How do water rates change when conservation is enacted?
Conservation requirements mean less water used, less revenue for utilities
Revenue recovery accomplished through drought surcharges (right)
Flat rate increase to fixed charge
Over half of drought surcharges work this way (Feinstein 2018)
Cutbacks
Monthly bill
increases

## Slide 16: Household water demand
Unit of measure for residential demand is household
Start with median per-person-per-month water consumption in non-drought years
Reported by SWRCB

## Slide 17: Historical Curtailment Decisions
5% reduction
25% reduction

## Slide 18: Alternative Curtailment Decisions
15% reduction

## Slide 19: Water bill for household income $47,500
5%
5%
15%
25%
Baseline
Alternative
Example water bill per month for household making $47,500/year
Light line: monthly bill for historical decisions
Dark line: monthly bill for alternative decisions
Takeaway: droughts increase water rates & increase is dependent on utility decision making
15%

## Slide 20: Who experiences these changes?
Annual change in water bill pre-drought vs. during-drought broken down by income class

## Slide 21: Who experiences these changes?
Bills go up for lower-income households
Fixed charges make up a large proportion of their bills

## Slide 22: Who experiences these changes?
Bills go up for lower-income households
Fixed charges make up a large proportion of their bills
Bills go down for high-income households
Amount saved by reducing water use > added fees

## Slide 23: Who experiences these changes?
Improving conservation policies can reduce burden on households

## Slide 24: Ongoing work…
Designing progressive revenue recouperations
Building infrastructure (desalination plant, recycled water, groundwater storage/recovery)
Dependence on household size, income, distributions
Designing low-income water rate assistance
Water access

## Slide 25: The Impact of Droughts on the Human Right to Water in California
Ben Rachunok, PhD
rachunok@stanford.edu
Questions

## Slide 26: Household water demand
Adjust baseline water use based on household income
Using price elasticity of water demand
“Given a 1% increase in my income, how much more water do I consume?”
Lots of work by our friends in the economics world trying to estimate this value. We use 0.1
Elasticity value is slope of the line

## Slide 27: Household water demand
Elasticity value is slope of the line
Water use for median income: 100G/month
EXAMPLE
What’s the water use for someone making 150% of median income?
50% increase in income
Change in Income x Income Elasticity = Change in Quantity
50% increase x 0.41 = 20.5% increase in water use
= 120.5 G /month

## Slide 28: Household water demand
Use this to adjust water uses for 16 different income classes:
  Household incomes of $7,500/yr all the way to up to $250,000+/yr
Calculate average size of households in each income class
Multiply income-adjusted per-person water use by household size to get a household water use
Elasticity value is slope of the line

## Slide 29: To start: retrospective of 2012-2016 drought
Many more shortfalls unadjudicated
  There wasn’t enough water but the water rights holders didn’t ask the state to step in
Fully Appropriated Stream Systems (FASS) mean the ‘average’ streamflow ≈ total water rights
Red: No new water rights can be issued
Blue: No new summer water rights can be issued
Last updated in 1998 when California had 20% less people

## Slide 30: Water Balance
Volume of water stored at t+1
Volume of water stored at t
Surface Water Sources
Groundwater
Natural inflow to reservoir
Demand (adjusted)
Net Reservoir Evaporation
Environmental outflow
Spillage (if necessary)